## Slide 1: Steps to download a firmware to GP device

## Slide 2
Install ST DFU driver
Switch to download mode, the device will become a DFU device, which needs ST DFU driver supported. Install a proper one according to your windows version.

## Slide 3
Run FirmwareDownloader.exe

## Slide 4
A GP device will be detected if plugged, which is in normal mode

## Slide 5
Click button to switch to download mode, then a device in download mode will be detected.

## Slide 6
Click button to select a firmware to be downloaded.

## Slide 7
The upgrade button will be enabled. After clicking it, a confirming message will be prompted.

## Slide 8
Start upgrading

## Slide 9
Unplug and then plug the device to PC again, the GP device will be switched to normal mode. The button to activate the display firmware will be enabled.

## Slide 10
Click the button to activate the display firmware. After several seconds, a message will be prompted if successful.